## Slide 1: A Rough Moving Points Filtering Method in Lidar SLAM
Group members:
Kevin Sinaga
Rigel Madraswalla
Samson Braun
Zuchen Zhang *All members have completed TRACE

## Slide 2: Overall Goals
Learn LeGO-LOAM, A-LOAM and LOAM, and compare the difference.
Have understanding of data set provided.
Find and implement some aspects that can be improved for LeGO-LOAM.
Implement a moving object filter to make map cleaner

## Slide 3: Background on the Basic Algorithm
We selected A-LOAM as our starting point
  It is simple to implement
  Does not involve the complex mathematical processes involved in loop closures
  Additionally, it is fast, and the only necessary input is a single Lidar point cloud, which was taken from the car_RGB dataset
  Highlights the strengths and failure points of basic lidar SLAM
Lacks many features of a more complex system like LeGO-LOAM
  Ground point extraction or segmentation
  Option to integrate IMU
  Loop closures

## Slide 4: Lidar Odometry
Feature point extraction
  C defined to evaluate smoothness of the local surface
  Results sorted by smoothness, feature points selected by excluding:
    Points which do not pass the threshold c values for edge or planar points
    Points surrounded by other feature points or exceeding the set limit number of points for a region
    Planar points where the plane runs near parallel to the laser
    Edge points on the boundary of occluded regions
The equation for local smoothness [1]
Image from the paper showing a) a point B which is on a plane unsuitable for precise measurements and b) a point A on the edge of an occluded region which may be observable from a different scan [1]

## Slide 5: Lidar Odometry
Finding feature point correspondence
  Algorithm estimates the motion of the vehicle within a given sweep, reprojects the point cloud at the end of the sweep
  Matches points from the new sets of edge and planar points to past reprojection
  Distance between a feature point and its correspondence is calculated
An illustration of identifying edge lines and planar patches as correspondence where j is the nearest point to the feature point in the current scan (shown as the orange line). In a) the case of an edge point, another point l is found as the closest neighbor on one of the two consecutive scans (shown as the blue lines). In b) for a planar point, the same process is done to find j, and l is found as the closest point in the same scan, m as the closest in a following scan [1]
A graph depicting the collection of a point cloud Pk, and its reprojection in green during the following sweep, shown in orange [1]

## Slide 6: Lidar Odometry
Motion estimation
  Assumes constant angular and linear velocities during a sweep
    Corrects for motion within a sweep using linear interpolation
  Employs the Levenberg-Marquardt algorithm to solve the lidar motion problem
    Frequently used to solve non-linear least squares problems
      Iteratively reduces the sum of the squares of the errors between the function and measured data by updating parameter values*
      Combines gradient descent and the Gauss-Newton Method [3]
    Runs until convergence is found or it hits the maximum number of iterations
*taken from The Levenberg-Marquardt algorithm for nonlinear least squares curve-fitting problems
The final equation given by the Levenberg-Marquardt method [1]
Example image of gradient descent from https://blog.clairvoyantsoft.com/the-ascent-of-gradient-descent-23356390836f

## Slide 7: Lidar Mapping
Running at 1Hz, the mapping algorithm runs once per sweep
Takes undistorted point cloud and estimated motion during the sweep
  Matches new cloud with previously generated world coordinates
Feature points extracted similarly to before
  10 times the number of feature points from odometry, which ran at 10Hz
  Map stored in 10m cube sections
Orientation matching also similar to odometry, again using the Levenberg-Marquardt algorithm
A visualization of the matching algorithm in mapping [1]
Illustration of the pose estimation for the mapping [1]

## Slide 8: Interesting Points from the Paper
Data taken in areas with significant and clear features yield better results
  Reduces drift
  Our data have good conditions
  Vegetation seems to be difficult for the algorithm
    Point matching is less clear without planar features or consistent edges
The authors later used a Kalman filter to integrate the IMU, and found reduced motion estimation error
Objects at greater distances tend to be seen as smoother
  These objects have a lower point density
    Also less important in the mapping
  However this poses an issue for objects as they get closer or further away, as their features points begin to change
Tables showing the results from the paper in different environments on the top as well as with IMU integration on the bottom [1]

## Slide 9: Codebase Structure
Chose A-LOAM implementation due to its ease of understanding
  “This code is clean and simple without any complicated mathematical derivation or redundant operations.” - Generation Robots
scanRegistration.cpp
  Point of interpretation for the raw PointCloud data from LiDAR
  Feature extraction (corners & flat surfaces) on current scene
laserOdometry.cpp - 10Hz
  Feature comparisons on consecutive frames
laserMapping.cpp - 1 Hz
  Interprets the movement of the LiDAR using odometry, publishes & updates a world map

## Slide 10: A-LOAM Demo
Notes: Ease of analyzing/running the code

## Slide 11: A-LOAM Failure Points
A-LOAM; 1 Lidar
GPS
Over time, position drifts slightly
A-LOAM does not:
  Employ loop closures
  Accept input from any other sensors
Easily implementable, but not robust
Image Source: https://www.roboticsproceedings.org/rss10/p07.pdf

## Slide 12: Loop Closures
The A-LOAM algorithm lacks any implementation of loop closures
  This results in drift throughout the processing of the data, which could be reduced as there are two loops with significant overlap in the dataset provided
  We would like to attempt to implement a loop closure process within the existing A-LOAM framework, in order to determine the advantage this gives in reducing drift
The data in car_RGB are ideally suited to loop closure given the high degree of overlap in the loops as the car retraces its path along Commonwealth
Can be implemented using visual data, or using the PointCloud data itself, as is the case in LeGO-LOAM

## Slide 13: LeGO-LOAM a lightweight and ground-optimized lidar odometry and mapping method
System overview of LeGO-LOAM[2]
Results of LeGO-LOAM blocks[2]
[2]: LeGO-LOAM: Lightweight and Ground-Optimized Lidar Odometry and Mapping on Variable Terrain

## Slide 14: Ground Point Extraction
Project point cloud to range image
A column-wise evaluation of the range image, which can be viewed as ground plane estimation, is conducted for ground point extraction before segmentation.
(The paper does not assume the ground is ﬂat. )
Points regarded as ground are given “ground” tag and not used for segmentation, and only remaining points are divided into different clusters.
Ground point extraction schematic
Image Source: https://www.google.com/url?sa=i&url=https%3A%2F%2Fwww.youtube.com%2Fwatch%3Fv%3DnXlqv_k4P8Q&psig=AOvVaw1E6CZgUCo04f7wgzZIfYV2&ust=1586466718020000&source=images&cd=vfe&ved=0CAIQjRxqFwoTCMC8w6Hf2egCFQAAAAAdAAAAABAO

## Slide 15: Segmentation
Group points in range image into many clusters (invoked from other paper)
Omit the clusters that have fewer than 30 points
Only the points that may represent large objects, e.g., tree trunks, and ground points are preserved for further processing
Only preserved points are saved in the range image
Results after segmentation step[2]
[2]: LeGO-LOAM: Lightweight and Ground-Optimized Lidar Odometry and Mapping on Variable Terrain

## Slide 16: Feature Extraction
To evenly extract features from all directions, we divide the range image horizontally into several equal sub-images
We call the points with c larger than cth edge features, and the points with c smaller than cth planar features.
Select strongest edge features and planar features, features with maximum or minimum c values.
Reflection:
When ri is at the denominator, further features trend to be judged as planar features, as you can see for further tree trunks. I think it may not be reasonable.
Can we make the threshold cth a floating value to make the algorithm adaptive to varying environment?
Is it possible to traverse the range map by a window, i.e. extract features on a higher level? Convolution?
As most edge features distribute near to the lidar, what if they are moving objects? I think it would be better if edge features are evenly distributed along the distance.
Results of feature extraction and selection, in(d), edge features are green and planar features are pink. In (e) strongest edge features are blue and strongest planar features are yellow[2]
[2]: LeGO-LOAM: Lightweight and Ground-Optimized Lidar Odometry and Mapping on Variable Terrain

## Slide 17: Lidar Odometry
The lidar odometry module estimates the sensor motion between two consecutive scans
Feature matching
Label matching
Two-step Levenberg-Marquardt Optimization
Reflection:
As we can see further trunks are regarded as planar features, while nearer ones are viewed as edge features. In this case, it may not be possible to match further trucks when they get closer, especially when we drive fast.
[2]: LeGO-LOAM: Lightweight and Ground-Optimized Lidar Odometry and Mapping on Variable Terrain
Lidar Odometry procedure[2]
Feature selection[2]

## Slide 18: Reflection on Lidar Odometry (continued 1)
Due to stereo, objects nearer will move faster than those further from the perspective of lidar. In this case I think features on ground could be hard to match. As you can see they don’t have many intersections.
Most planar features are on the ground.
Stereo schematic
Source: http://www.cse.psu.edu/~rtc12/CSE486/lecture08.pdf
Schematic of 2 consecutive scans on the ground
Feature Extraction results[2]
[2]: LeGO-LOAM: Lightweight and Ground-Optimized Lidar Odometry and Mapping on Variable Terrain

## Slide 19: Lidar Mapping
Match current features with previous features, either of the approaches below.
Choose the feature sets whose sensor poses are within 100m of the current position of the sensor. The chosen feature sets are then transformed and fused into a single surrounding map generated at the last instant
Integrate pose-graph SLAM into LeGO-LOAM. The author thinks the pose estimation drift of the lidar mapping module is very low, so we can assume that there is no drift over a short period of time. So the matching is only between current feature sets and a group of past feature sets.

## Slide 20: Difference between LeGO-LOAM and LOAM
LeGO-LOAM has a segmentation procedure, which filters out clusters having less than 30 points. It improves processing efﬁciency and feature extraction accuracy.
LeGO-LOAM has a unique type of feature, ground detection. Ground points are exclude from edge feature extraction and are only for planar feature extraction.
Map storage: LOAM saves a single point cloud map, while LeGO-LOAM saves each individual feature set.

## Slide 21: Results in the LeGO-LOAM paper
Number of feature points is reduced considerably.
Most edge feature points are not on the ground
Still many planar feature points on the ground
Edge and planar features are colored green and pink, respectively. The features obtained from LOAM are shown in (b) and (c). The features obtained from LeGO-LOAM are shown in (d) and (e).
There are grass and trees in the way, which will result in unreliable feature extraction in LOAM. As a result, LOAM’s pose estimation diverges.[2]

## Slide 22: Results of running LeGO-LOAM
drifting
Using IMU raw data
Diving into the ground

## Slide 23: Results of running A-LOAM and LeGO-LOAM(Continued 1)
LeGO-LOAM generate a map with less features, and it looks clearer. But it is also omitting a lot of features on cars. I think we can figure out what the typical difference is between cars’ data (shouldn’t omit) and leaves’ data (already largely omitted) and do some modifications.

## Slide 24: Results of running A-LOAM and LeGO-LOAM(Continued 2)
Neither A-LOAM nor LeGO-LOAM is able to filter out moving objects

## Slide 25
A Possible Way to Remove Moving Objects
As LeGO-LOAM does feature matching to estimate Lidar Odometry and Integrate Lidar Odometry into Transform between scans later, and the map generated is not bad. So we imply that those matched features is likely to be on stationary objects. Because if those features are on moving objects, the Lidar Odometry will have considerable error, so as the map.
We extracted those matched corner features (corner features are named edge features in the paper) and only used them to generate map. The modification to the code is basically publishing matched corner feature points instead of all feature points to construct the map.
As is shown in the video, matched feature points are on both moving and stationary objects, so this approach almost doesn’t help. Transform precision is decreased as well.

## Slide 26
Another Possible Way to Remove Moving Objects
According to our observation, a large number of ghosting happened near to our car. In addition, lots of moving objects moved in the same direction as our car did in most cases.
This kind of moving objects are likely to be seen in both of 2 consecutive scans. So we set a threshold range, which is shown as the circle. We transformed all corner features and planar features scanned at time t+1 and within this range to frame of time t respectively. Then we examined the squared distance between transformed feature points of t+1 and all feature points of t. If the result is less than a threshold, the feature point will be evaluated as being on moving objects, and it will be popped out from point set used for map construction.
However, stationary features with in the range are filtered out as well. So we find it performance similar to filtering out all points with in the range…

## Slide 27
Filtering Out Moving Features Within a certain Range
Corner feature filtering results
Filtering out ghosting corner features with in 6 meters. Green points are remaining corner features, while purple points are all corner features extracted, before filtering. Only green points will be used for mapping later. As you can see from 1:10, an approaching car is filtered out, so it won't show up on the map. But as you can see from 0:25 and 1:30, corner features with a distance to our car larger than 6 meters can not be filtered. The range needs optimization, if it is too large, the quality of map will decrease, while if it is too small, the filter will not make much sense.
Filtering out ghosting planar features with in 6 meters. Green points are remaining planar features, while purple points are all planar features extracted, before filtering. Only green points will be used for mapping later. As you can see from 1:07, an approaching car is filtered out, so it won't show up on the map. But as you can see from 0:22 and 1:30, planar features with a distance to our car larger than 6 meters can not be filtered. The range needs optimization, if it is too large, the quality of map will decrease, while if it is too small, the filter will not make much sense. The map construction occluded outlier feature points, as I don't know what they are after inspecting the source code.
Planar feature filtering results

## Slide 28
Filtering Out Moving Features Within a certain Range
Filtering out both corner features and planar features
Filtering out both ghosting planar features and ghosting corner features with in 6 meters. Green points are remaining features, while purple points are all features extracted, before filtering. Only green points will be used for mapping later. As you can see from 1:22, an approaching car is filtered out, so it won't show up on the map. But as you can see from 0:38 and 1:46, features with a distance to our car larger than 6 meters can not be filtered. The range needs optimization, if it is too large, the quality of map will decrease, while if it is too small, the filter will not make much sense. The map construction occluded outlier feature points, which is a type of points independent from corner feature points and planar feature points, as I don't know what they are after inspecting the source code.
As you can see that most features within a 6 meter range to the car is filtered out. But the truck in front of us was consistently mapped, as features on the truck is out of the range so they can not be filtered out. The range needs optimization, if it is too large, the quality of map will decrease, while if it is too small, the filter will not make much sense. The map construction occluded outlier feature points, which is a type of points independent from corner feature points and planar feature points, as I don't know what they are after inspecting the source code.

## Slide 29
Reflection and future exploration directions
The value of the range should depends on the situation our car is in. For example, if the road is narrow, the range value should be lower, so buildings on the side can still be mapped clearly, vise versa. But if the range is too large, this approach could be computationally expensive and may not able to run in real time.
A further exploration of this approach could be control system design to make it a dynamic value to get optimal filtering.
To reduce computation expense, a fast-matching approach should be designed. I think it would be likely to be based on data structure of Pointcloud and its indexing.
Anyway, I think it is rough and hard to match feature points based on point-wise matching to filter out moving feature points. I think moving objects(features) detection should be based on some kind of high level abstraction of data, probably a patch in Pointcloud?
Develop an algorithm that enables modification of frames already mapped.

## Slide 30: References
[1] LOAM: Lidar Odometry and Mapping in Real-time by Ji Zhang and Sanjiv Singh
[2] LeGO-LOAM: Lightweight and Ground-Optimized Lidar Odometry and Mapping on Variable Terrain
[3] The Levenberg-Marquardt algorithm for nonlinear least squares curve-fitting problems
We generated a bag file with out image based on provide bag file, which considerably shrunk in size and we used this for experiments: https://drive.google.com/file/d/1GWFps5dEd4riRmx3ijPzhOqwtpUq41cw/view?usp=sharing
Gitlab repository: https://gitlab.com/Zuchen_NEU/eece5554_roboticssensing